Bexhill to Hastings Link Road

Non-Material Amendments Summary – NMA S24 H36

December 2012

Introduction

Following the granting of planning permission for the Bexhill Hastings Link Road in 2009, opportunities to optimise the design have been taken and, as a consequence, detailed refinements have continued to be made. Many of these refinements will be scrutinised and considered by the Local Planning Authority (LPA) as part of the process of discharging planning conditions. However, there are some changes proposed which will require the approval of the LPA as “non-material amendments” (NMAs). This paper prepared in support of the NMA application is intended to describe and explain the changes together with the reasons for them.

The proposed changes fall into two categories:

-	Measures which will to avoid construction of some structures, and

-	Measures which will reduce the scale of the construction works whilst still maintaining the function of the road.

Structure Related NMAs:

It has been found to be possible to maintain a number of existing bridges rather than build new

replacements. This has the beneficial effect of reducing the impact on the existing environment both in terms of construction activities and additional infrastructure. This NMA planning application relates to the following:

S24 – Deletion of Proposed Watermill Stream Crossing

The approved scheme provides for separate bridge crossings over the Watermill Stream for horses and cyclists/pedestrians; the former using an existing bridge and the latter a new structure less than 30m to the south.  A modification to the Greenway alignment, allowing pedestrians and cyclists to use the existing bridleway bridge at Watermill Stream, has the benefit of removing the need for the new bridge. The existing bridge is adequate for the volume of users projected while deletion of the new structure will reduce visual impact and construction disturbance. A consequent small re-alignment of the cycle/footpath is also proposed.

Highway Related NMAs:

A re-examination of the detailed road design has enabled some revisions to be proposed which will reduce the impact of construction works in some places whilst maintaining the full function of the road. The following proposed NMAs will all contribute to achieving a smaller impact on the surrounding countryside. These changes also have the added indirect benefit of influencing driver behaviour and so reducing maximum actual road speeds.  Changes to the design of the junction with Crowhurst Road will also actually improve through flows through it whilst reducing its visual scale in the landscape.

This NMA application relates to the following such change:

H36 – Combining of Greenway North of the Watermill Stream

This section of the proposed Greenway lies between Acton’s Farm and Adam’s Farm and is somewhat over 300m in length. The approved scheme provides for separate equestrian and cycle/paths which then merge at their eastern ends. The equestrian route is somewhat to the north of the cycle/footpath and links with an equestrian only path that runs northwards and over the Link Road to Hillcroft Farm via an overbridge.  Combining the greenway and bridleway over the section from the Watermill Stream bridge to the approximate chainage line 3700 allows for a decreased land take and an optimised cross section for the paths - thus reducing impact both during and after construction.

The specification of the revised section of the Greenway will be in accordance with that set out in the appended technical note H001 for a combined bridleway and cycleway/footway.