BEXHILL TO HASTINGS LINK ROAD

REVIEW OF CONTRACTORS DELIVERABLES

Drawing/Document reviewed:	Approval in Principle for S09 Watermill Stream Underbridge

Document Reference:		B1297000-PH2/1600.06a/0009 (rev 0)

Date of Receipt:			28 August 2012

Date of Review by TAA:		7 September 2012

Date of Review Response:

The Drawings/Documents have been reviewed. The submission is NOT accepted.

The following comments below have been identified.  Please review all comments above, revise the drawings/document as appropriate, and provide a response to comments.

| AIP | Review Comment | Contractor’s Response |
| --- | --- | --- |
| Cl 3.7.1 | Proposal for inspection of the environmental noise barrier using an underbridge unit is not consistent with that given in Cl 3.7.2, (See below). |  |
| Cl 3.7.2 | The above clause indicates that the environmental noise barrier would be inspected etc from an underbridge unit located on the carriageway, but Cl 3.7.2 states that the environmental noise barrier would need to be removed for the operation of the unit. Consider demountable top section to environmental noise barrier, (accessible from deck), so that underbridge unit can operate unimpeded over the top of the steel parapet. Details are not required at this stage, but the principle needs to be determined. |  |
| Cl 4.1.2 | Original AIP stated 45units of HB loading, ( see emails dated 1 Sept 2009 between Jacobs, ESCC & Mott McDonald) |  |
| Cl 4.1.5 | Clarify how surcharging of approach embankments would be carried out without conflicting with the principle of overspanning the existing stream and not interfering with its channel. |  |
| Cl 4.3 | The original AIP included two Departures from Standard, re CHE Memo 227/08 & IAN 96, (these had been agreed in advance and clarified that a sand asphalt layer was not normally required, and impregnation was also not required for BHLR structures. Please reinstate these as it clarifies what is proposed. |  |
| Cl 5.1 | Amend ‘Retaining walls’ to ‘Wingwalls’ |  |
| Cl 6.3 | Include that 20mm differential movement between the piled structure and the approach embankments will be taken into account, and that provision will be made for this vertical movement for the N2 parapet and environmental noise barrier at the interface of the free standing wingwall with the piled section. |  |
| Cl 10 | Please leave a space for any required Conditions/Amendments by TAA. |  |
| Appendix A TAS | Implementation BDs for BS 5400 are incorrect , (ie ‘See BD1’,etc) Include IAN 104/07 |  |
| GA Drg | Drawing Number & Title on the drawing is not consistent with that stated on Appendix B Cover Sheet. What is the basis for 600mm wide parapet plinths? Clarify provisions for relative movements between piled wingwall and free standing section of wingwall, how will parapet/noise barrier accommodate this? |  |