BEXHILL TO HASTINGS LINK ROAD

REVIEW OF CONTRACTORS DELIVERABLES

Drawing/Document reviewed:	Approval in Principle for S15 Crowhurst Road Underbridge

Document Reference:		B1297000-PH2/1600.06a/0015(rev 0)

Date of Receipt:			   2  October 2012

Date of Review by TAA:		  29 October 2012

Date of Review Response:

The Drawings/Documents have been reviewed. The submission is NOT accepted.

The following comments below have been identified.  Please review all comments above, revise the drawings/document as appropriate, and provide a response to comments.

| AIP | Review Comment | Contractor’s Response |
| --- | --- | --- |
| General | As the original PC beam piled integral structure has been revised to a RC box structures many of the comments made regarding the 2009 AIP are no longer relevant. The AIP submitted is for a box structure with the roof slab directly below the road surfacing. The ‘Contractor’s Response’ has indicated that during detailed design the option of reducing the excess headroom provision and providing filling above the box would be investigated further. An addendum to the AIP would be required to cover this change to the proposed structure. The ESCC Structures Manager has concerns regarding bird access and roosting positions on the externally mounted 375mm dia drainage pipe, in addition to it detracting from the appearance of the structure. |  |
| Cl 1.2 | Still a query regarding the permitted traffic speed for Crowhurst Road, (ESCC had informed me in 2009 that it was 60mph, rather than the 40mph stated in the AIP). Google shows the road to be derestricted from just outside of Crowhurst until and including Queensway. |  |
| Cl 1.3 | The 2009 AIP and the current AIP for the adjacent Railway Bridge included reference to the structure being within the boundary of a Site of Nature Conservation. |  |
| Cl 3.6 | Clarify that the proposal for safety fencing on the verges of Crowhurst Road will be confirmed or otherwise by RRRAP, ( ie as stated in the ‘Contractor’s Response’. (Note that TD 19/06 Cl 3.102 requires a safety barrier to prevent an errant vehicle impacting the end of a structure.) The provision of 45degree splayed wingwalls instead of wingwalls parallel to the BHLR would probably avoid the need for safety fencing on Crowhurst Road. |  |
| Cl 3.8.1 | Remove reference to ‘existing structure etc’ in title. Reconsider XC3/XC4 for box roof slab soffit. Reconsider XC3/XC4 for box walls exposed face. |  |
| Cl 4.1.1 Cl 4.1.2 Cl 4.1.3 | Include BD 31/01 in addition to BD 37/01 |  |
| Cl 4.2.1 | Add IAN 117/08 Rev 2. |  |
| Cl 6.3 | Add that 20mm differential settlement between the structure and approach embankments will be provided for. |  |
| Cl 8.1 | Drawing title is not consistent with that shown on the drawing. |  |
| Appendix A TAS | Include TD 9/93, (was in 2009 AIP and is in current AIP for Railway Bridge). Include BD 63/07. |  |
| GA Drg | Drawing title not consistent with Cl 8.1. |  |