LANDSCAPE SPECIFICATION

(For use with ESCC Conditions for Landscape Works)

1.	(PRELIMINARIES)

1.1  	Scope of Landscape Contract

The works described in this contract comprise:

1.1.1	Completion Dates and Defects Liability

All works: trees/shrubs/grass shall reach practical completion by .........

All hard works shall reach practical completion by  ......

Interior planter/s shall reach practical completion by .......

A defects liability and maintenance period will run from the date of Practical Completion for ................... calendar months until Final Completion is reached.

1.1.2	Hours of Work

The Contractor will only be permitted to work on the site between the following hours:-

07.30 – 18.00 Mondays to Fridays

07.30 – 13.00 Saturdays

excluding Bank Holidays unless authorised by the Contract Administrator.

1.2	Drawings

The work is to be carried out in accordance with Drawing Nos.

........................ and this specification and conditions of contract.

The Contract Administrator may produce further drawings if he deems it necessary for the Contractor's guidance, instruction or assistance.

1.3	Sub-Letting

The Contractor shall not sub-let any portion of the works without written consent of the Contract Administrator.

1.4	Loss of Materials

The Contractor shall include for Insurance to adequately cover for the loss or damage of materials from the site until the date of practical completion of the works as certified by the Contract Administrator. The Contractor will be required to immediately replace all lost or damaged (maliciously or otherwise) plants or materials at no additional charge to the contract up to the date of certified practical completion.

1.5	Materials, Labour and Plant

1.5.1	The Contractor shall provide everything necessary for the proper execution of the works including all transport, plant, tackle, machinery, materials and labour of every kind.

OR

The Contractor shall provide everything necessary for the proper execution of the works including all transport, plant, tackle, machinery, materials and labour of every kind apart from items of attendance listed on page 4 of the form of tender described as provided by the Main Contractor.

1.5.2	The Contractor shall allow for maintaining and removing on or before completion, all plant and tools, necessary for the execution of the works.

1.6	Temporary Site Name Board

EITHER

The Contractor shall allow for providing a temporary site plywood board 1.300 x 0.3m, for the display of the consultant's information. The Contract Administrator shall supply

1 no. self-adhesive PVC label to the Contractor who shall fix this to a panel mounted and nailed to 2 no. timber posts 75 x 75mm x 1200. Posts to be set upright and 500mm below ground level. Position shall be agreed on site with the Contract Administrator.

OR

The Contractor is to allow in his price for providing a temporary site name board to conform to the standard layout prepared by the Contract Administrator. The Board shall have an exterior quality plywood panel size 2400 x 2400mm with projecting margin and adequate timber framing.

The Contract Administrator will supply two self-adhesive flexible PVC labels bearing the clients name and project designation and the other showing the Contract Administrators name and the Contractor shall allow for fixing these to the Board. £

Other areas are provided on the board for the Contractors own name.

1.7	Materials and Articles to be Approved

1.7.1	The Contractor is to make provision for supplying samples of all materials, proposed to be used for the works. The Contractor must give 48 hours notice to the Contract Administrator of the provision of these samples and no further materials are to be brought onto the site until the samples have been approved by the Contract Administrator. Any materials brought onto the site prior to such approval, will be deemed to have been so at the Contractor s risk, and must be removed if requested at no cost to the Contract.

1.7.2	After approval of the samples supplied, all subsequent materials must be of similar quality and the first sample must remain intact until all deliveries are completed in order to make comparisons of quality.

1.7.3	The Contractor shall, if required, furnish the Contract Administrator with satisfactory evidence that materials are of the origin and quality specified and shall provide samples for approval and for testing by the Contract Administrator, who shall have power to reject all materials which do not correspond with approved samples.

1.7.4	All lorries or trucks calibrated to convey soil, sand, ballast, clinker, etc., to the site shall carry only that amount calibrated thereon. No payment shall be made to the Contractor for the supply of materials unless all delivery tickets have been properly signed by the Contract Administrator, and no alterations have been made thereon.

No claims arising from delay in this respect will be entertained.

1.8	Wheeled Equipment

Only approved pneumatic-tyred wheeled equipment will be permitted unless carried on pneumatic-tyred transporters, or unless otherwise approved by the Contract Administrator.

There will be no access to the site for vehicles weighing over

10 tonnes without prior agreement with the Contract Administrator.

1.9	Use of Site

EITHER

The Contractor is not to use the site for any purpose other than that of carrying out the works, and he is to obtain the approval of the Contract Administrator for the siting of all spoil heaps, temporary roads, rail or sleeper tracks, paths, sheds, offices, and other structures.

OR Sub-Contractor 's paragraph

The Contractor shall not use the site for any purpose other than that of carrying out the works, and he is to obtain the approval of the Main Contractor  for the siting of all spoil heaps, structures, storage areas, temporary access, etc.

1.10	Area to which the Contractor will be Confined

The area of land affected by this contract and which is available for use by the Contractor for the execution of this Contract will be defined by the drawings listed in clause 1.2. The Contractor shall confine his workforce, his temporary buildings, stores and everything pertaining to this contract within these limits.

1.11	Access to the Site and Works

The Contract Administrator and his representatives shall have access at all reasonable times to  (1) the works; and (2) any premises where the Contractor is preparing or making anything for the works; the Contractor in placing his orders, shall secure similar rights of access to any premises where products for use on the works are being prepared or made.

1.12	Protection of the Highway and/or of Private Roads

1.12.1	Traffic Safety and Control

1.12.2	The Contractor shall where works are on or adjacent to highway land comply with the recommendations in Chapter 8 Traffic Safety Measures for Road Works of the Traffic Signs Manual published by her Majesty's Stationery Office.

1.12.3	In particular, Sign No. 564 (Road Works) from the above mentioned manual must be displayed at all times, and where vehicles obstruct one lane of the carriageway, cones are to be positioned at either side of the obstruction extending for a distance of 75 metres.

1.12.4	Public Highways to be Kept Clean

All public highways which are being used by the Contractors', Sub-Contractors' or Suppliers' vehicles in connection with the works shall be kept clean and free of dirt and mud.

1.12.5	Where the highway construction is still within defects period, prior to the Contractor commencing works, a joint inspection to agree and record the condition of the carriageway, footway and all associated new works shall be made with the Contractor and a representative of the County Highways department.

1.12.6	The Contractor shall provide all cross-overs necessary to prevent damage to public or private carriageway, footway, kerbs or drains, also any shoring and strutting which may be necessary. Any damage shall be reinstated to the satisfaction of Contract Administrator. In the case of private land, any damage shall be reinstated to the reasonable satisfaction of the owner.

1.13	Private Land and Property Adjoining the Site

1.13.1	The Contractor shall not enter onto any private land for any purpose in connection with the Contract without the prior approval in writing of the Owner and the Contract Administrator. Where any accommodation work is to be carried out on private land the owner/ occupier must be consulted in advance.

1.13.2	The Contractor shall exercise care in working in the vicinity of fences, hedges, trees and the like which are to remain and he shall make good any damage which may occur to any property, however caused.

1.14	Nuisance to Owners Within or Adjacent to the Contract Area

The Contractor shall take all necessary precautions to prevent danger, nuisance or inconvenience to the owners, tenants or occupiers of properties within or adjacent to the works area or haulage routes, and the public generally, and shall at all times keep all roads, streets, private entrances, verges, footpaths and paved areas, drains and sewers in the area of the works and haulage routes in a safe, clean and passable state. All waste or superfluous material shall at his own expense be cleared away as soon as possible by the Contractor to his place of deposit.

1.15	Protection of Work and Materials

1.15.1	The Contractor shall be responsible for the safety of the works during the execution thereof until completion and of all plant, materials and other property on the site for the purposes of the work.

EITHER

1.15.2	All plant materials brought to the site during inclement weather or frost, shall be heeled in (if ground conditions are suitable) or protected by straw bales, or other approved means.

OR Sub-Contractor's paragraph

The Landscape Sub-Contractor shall maintain the indemnities as listed in Clause 27 (iii) (iv) J.C.T. Conditions of Contract.

1.16	Incidental Damage

The Contractor is to make good any and all damage done to all existing items and features on the site, including buildings and all fixtures and fittings, fences, gates, drives, pavings, vegetation of all types, services of all types, land and any other articles in the course of these works at no cost to the contract.

1.17	Completion and Clearance of Sites

At both practical and final completion the Contractor is to remove all plant, sheds and implements, to excavate as necessary and cart away all surplus materials and debris of any kind from the whole of the site

EITHER

raking, forking beds or compacted areas of soil, levelling up, and cultivating as may be necessary.

OR

and weeding prior to applying top up mulch. Where no top up mulch is required the surface shall not be disturbed by hoeing or forking over unless by agreement with the Contract Administrator

The whole of the works should be completed and the site left in perfect order to the entire satisfaction of the Contract Administrator.

1.18	Removal of Rubbish

The Contractor shall remove all surplus materials and rubbish to his own place of deposit, including for haulage and any fees payable, from time to time as works proceed.

1.19	Registration of Waste Carriers

The Contractor is required under THE CONTROLLED WASTE (REGISTRATION OF CARRIERS AND SEIZURE OF VEHICLES) REGULATIONS 1991 to register with the local waste regulation authority if he transports controlled waste. The Contractor is to provide proof of his registration to the Contract Administrator if asked to do so at any time.

The Contractor is to send a copy of his registration certificate to the Director, Transport and Environment and is to ensure that any amendments to the document are submitted as they are issued.

1.20	Accommodation for Workmen and Materials

1.20.1	The Contractor shall provide or make available adequate and suitable accommodation for workmen's messing.

OR

make arrangements for use of facilities with the client

(Tel: .........

The Contractor shall provide for the reception and requisite storage and safekeeping during and after delivery on the site of all materials (by whomsoever supplied) for the execution of the work.

1.20.2	The Contractor shall allow for providing, maintaining and removing on or before completion of the works any necessary temporary sheds for shelter and storage of materials described in 1.21.1.

1.20.3	The Contractor shall observe all appropriate regulations regarding storage of flammable materials, the arrangements for which shall be subject to the approval of the Contract Administrator. Where acetylene, oxygen, propane or other gas cylinders are to be used on the site, the Contractor shall provide and maintain a painted notice board, red letters on a white background size 600mm x 450mm which notice shall read "DANGER COMPRESSED GAS CYLINDERS". Such notice shall be securely fixed externally and prominently where gas cylinders are stored.

1.21	COSHH Regulations

The Contractor or his approved sub-Contractor shall not apply any substances hazardous to health to the site without agreement of the Contract Administrator and all such applications shall fully conform to the ESCC policy on the control of Substances Hazardous to Health including providing a written risk assessment if required to do so by the Contract Administrator.

1.22	PESTICIDE (including HERBICIDE USE)

EITHER

No herbicides shall be applied to this site.

OR

Where herbicides may be used the following shall apply:

1.22.1	All equipment and materials for herbicides application shall be used according to the manufacturers' instructions and all precautions are to be taken to protect the Contractor 's employees and the general public using the site. Spraying shall be done only in appropriate weather conditions. All herbicides shall be approved by the Contract Administrator before use. Great care must be taken at all times when mixing, and no surplus chemicals shall be disposed of on site. Spray equipment is not to be cleaned on site. The Contractor and his employees must at all times operate in accordance with the Control of Pesticides Regulations 1986, the current Food and Environmental Protection Act 1985, the Health and Safety at Work Act and the ESCC Pesticides Policy and Code of Practice (which is available to view at the Transport and Environment Office, County Hall, St Anne's Crescent, Lewes - Note: the ESCC code applies restriction over and above legislation) and any other relevant legislation.

The Contractor is to note that there is a special duty of care on sites to which the public have access.

1.22.2	Work

All workpeople are to be competent and experienced in all aspects of work on which they are engaged. All operatives engaged in spraying activities shall hold a certificate of competence as defined under the above Acts and Code of Practice and the Contractor shall produce such documentation for inspection by the Contract Administrator if requested.

1.22.3	Timing of Application

No pesticides including herbicides shall be applied without prior approval by the Contract Administrator to school sites or Elderly People's Resource Centres.

No herbicides shall be applied to these sites during periods when children or elderly are in occupation or arriving at or leaving the building or site. It is essential that no work is undertaken without the prior consent of the head teacher or managers. Consent shall be made by way of liaison by the Contract Administrator.

1.22.4	Records

The Contractor shall keep records of all herbicide application on the forms provided by the Contract Administrator as required under the Act, copies of which are to be given to the Contract Administrator for his retention within 48 hours of completion of the herbicide application.

1.22.5	Approved Pesticides

The Contractor will only be permitted to use Category 1A Substances listed in Appendix 8 of the current ESCC Pesticides Policy and Code of Practice as reproduced below.

Category 1A Substances Approved for Use

Active Ingredient	Approved Use

Alloxydim-sodium	Selective weed control

Ammonium sulphamate	Stump treatment

Asulam	Bracken control

Carbendazim	Worm control

Carbendazim	Fungicide

Derris (Rotenone)	Insecticide

Dicamba	Selective weed control

Dichlobenil	Total weed control

Dichlorophen	Moss control

Diflubenzuron	Brown Tail Moth caterpillar*

Ferrous sulphate	Moss control

Fosamine ammonium	Stump treatment

Glyphosate	Total weed control

Imazapyr	Total weed control

Iprodione	Fungicide

Mecoprop	Selective weed control (NOT weed and feed)

Metham-sodium	Dutch Elm disease

Propyzamide	Total weed control

Pyrethrins	Insecticide

Pyrethrum	Insecticide

Sodium chlorate	Total weed control (paths)

Triclopyr	Selective weed control

Triclopyr	Stump treatment

Warfarin	Rodent control

*  to be used only where the removal of larval tents is not practical.

1.23	Safety, Health and Welfare of Workpeople

The Contractor shall comply with the Health and Safety at Work Act 1974 and the Building (Safety, Health and Welfare) Regulations, 1948 and subsequent amendments having effect under the Factories Act 1961 including the construction (Health and Welfare) Regulations 1966 and the Management of Health & Safety at Work Regulations 1992 which require the Contractor to ensure safety on the site and to provide the Contract Administrator with any risk assessment that needs to be undertaken.

1.24	Precautions Against Spread of Fire

EITHER

No site fires shall be permitted.

OR

1.24.1	When such burning is permitted and undertaken, the Contractor shall avoid at all costs the spread of fire. It shall be the Contractor 's sole responsibility at the end of each working day to ensure that all fires are properly extinguished. Any damage to crops, vegetation or property belonging to the Employer or to any Third Party as a result of fires begun by the Contractor or his employees or representatives, shall remain the sole liability of the Contractor under the conditions of the Contract. The Contractor is deemed to have checked for services, permission from Local Authorities, etc.

No fires shall be lit within 3 metres of the spread of any tree or shrub. All burning sites to be agreed with the Contract Administrator.

1.24.2	The Contractor shall be permitted to burn only materials approved by the Contract Administrator. Materials that would not be approved under any circumstances would include:-

Rubber, plastics, asphalt, cables.

1.24.3	When burning vegetation the Contractor is to stockpile the material for a minimum of one week to allow drying out prior to burning in order that dense smoke can be kept to a minimum.

1.24.4	The Contractor is to have regard for the wind force and direction prior to lighting a fire to minimise smoke nuisance to adjacent residents. If at the sole discretion of the Contract Administrator the fire is causing a nuisance in any way the Contractor is to extinguish it immediately.

1.25	Temporary Services

EITHER

1.25.1	The Contractor shall be responsible for providing any temporary services required for the execution of the works. The Contractor may obtain temporary connection to The Employer's supplies but this shall be subject to the agreement of the statutory undertakers concerned and to the Contractor making the necessary applications and bearing the cost of any charges, including any necessary check meters and equipment for dispersing water/power.

OR Sub-Contractor 's paragraph

The Contractor shall arrange with the Main Contractor for the free and reasonable use, at his own risk, of such temporary services as may be required for the execution of the works including water, telephone and electricity for power and lighting, as supplied under the main contract attendance on page 4 of the form of tender provided by the Main Contractor.

1.25.2	Where a main building contract is in progress on the site the Contractor may negotiate for the use, at his own cost, of temporary supplies arranged by the main Contractor with the appropriate statutory undertakers, during the period of that main building contract only. Thereafter clause 1.26.1 will apply.

1.25.3	A tap to which a hose may be fitted shall/shall not be available in the building.

1.25.4	The Contractor shall provide his own hoses and fittings and shall ensure that all equipment is removed and taps locked when the Contractor is not on site.

1.26	Travelling

The Contractor shall include in his price for all travelling costs and travelling time to and from the site.

1.27	Workpeople

1.27.1	All workpeople are to be competent and experienced in all aspects of work on which they are engaged. The Contract Administrator reserves the right at his absolute discretion to dismiss from the site any workman employed by the Contractor, if in the opinion of the Contract Administrator such workman is not competent.

1.28	Foreman

The Contractor shall constantly employ an approved competent foreman on the works, and any instructions given by the Contract Administrator shall be deemed to have been given to the Contractor. The name of the foreman shall be supplied at the initial meeting with the Contract Administrator.

1.29	Importation of Labour

The Contractor shall allow for all or any costs arising from the importation of labour from any sources.

1.30	Specification and Plans

The foreman shall at all times have a copy of the specification and plans whilst on site.

1.31	Identification

The Contractor and his workpeople shall be required to carry an approved form of identification at all times when working on occupied sites.

The identification shall include the company name, address and telephone number, the company manager’s name, and the name of the cardholder.

The Contractor or any of his representatives including delivery personnel must report to the reception each time he visits the school to report his presence and departure.

1.32	Existing Plants

1.32.1	No existing trees, shrubs or other plants shall be removed or cut without written instructions from the Contract Administrator.

The Contractor shall take all precautions to protect, in the course of his work, all existing plant material from accidental damage.

1.32.2	No soil, spoil, constructional materials or rubbish shall be stored or tipped within ............ metres of existing trees.

1.33	Damage to Trees

Any of the existing trees on the site damaged in any way shall be subject to a penalty of £........ per tree, which shall be used at the Contract Administrator's discretion for replacement.

1.34	Statutory Undertaker's Service Lines

1.34.1	The Contractor shall comply with any requirements of the Statutory Bodies in relation to their services, and take all necessary precautions to avoid interference with, or damage to, any mains and services within the vicinity of the works. He shall make good any damage that may arise to the satisfaction of the Authority or Undertaking concerned.

1.34.2	Where new services have recently been installed as part of the construction contract, and where they are adjacent to proposed landscape works, these services will be shown on plans which shall be issued to the successful Contractor. They are to be defined on site and pegged out by the Contractor before works are commenced. The Contractor shall, after carrying out this check, be held responsible for damage to any services which he knows or could have been reasonably expected to know, to exist on the site.

1.35	Daywork

EITHER

Dayworks shall be authorised for payment at the sole discretion of the Contract Administrator. Any work to be included on Daywork sheets should be notified in advance to the Contract Administrator.

OR Sub-Contractor's paragraph

Dayworks shall be authorised for payment at the sole discretion of the Architect in accordance with the rules pertaining to Clause 11 (4) J.C.T. Conditions of Contract. Any work to be included on Daywork sheet should be notified in advance to the Contract Administrator. Daywork sheets must be submitted for signing to the Contract Administrator at the end of the week in question.

1.36	Visit the Site

The Contractor is advised to visit the site and surroundings so as to be thoroughly conversant with the position, conditions, character and extent of the proposed works and the means of access thereto and will be deemed to have done so prior to submitting his tender.

1.37	Commencement of Work

The Contractor shall commence works on site within four working days from the issue of the written instruction to commence, unless otherwise agreed in writing with the Contract Administrator.

1.38	British Standards

All goods, materials and workmanship not otherwise specified shall be in accordance with the latest British Standards where such exist and to the satisfaction of the Contract Administrator.

1.39	Overtime

No overtime shall be worked without notice to and the agreement of the Contract Administrator being given at least 48 hours notice before its commencement.

1.40	Contingency Sum

Allow the sum of £....... for contingencies to be expended or

deducted as directed by the Contract Administrator.	£

1.41	P.C. and/or Provisional Sums

The following P.C. and Provisional sums are to be included in the Tender Price and will be deducted in whole or in part from the Contract Price: NIL

1.42	Provision for Direct Payment Sums

The following sums are to be included in the Tender Price and will be deducted in full from the Contract Price: NIL

TOTAL Preliminaries and Contingencies:

Carried to Summary.

WORKS BY OTHERS

?

2.	THE WORKS

2.1	Notice of Intention

The Contractor shall give 48 hours notice to the Contract Administrator and agree with him his intentions to commence any of the following operations:-

2.1.1	Work Programme and Method Statements

The Contractor shall submit a programme of works and method statements to the Contract Administrator prior to the works commencing on site or at the initial meeting with the Contractor.  Dates shall be clearly set out showing when the Contractor intends to carry out the various aspects of the project from the start up to the date of practical completion.

2.1.2	Setting Out the Works

The Contractor shall be responsible for setting out all required works.

The Contract Administrator shall, either by dimensioned drawings or written instructions, give the Contractor the necessary information to enable him to set out the works.  The Contract Administrator shall approve such setting out prior to works proceeding, after which any inaccuracies shall be amended by the Contractor at his own cost.

2.2	Season

2.2.1	All work shall be carried out at an appropriate season and in weather conditions suitable for the operation.

2.2.2	Suitable weather conditions for planting shall mean mild and moist even in winter, when ground is moist and workable. Planting operations shall be suspended in periods of drought, when soil is frost bound or water logged, and in periods of persistent drying cold winds.

2.2.3	Suitable Conditions for Ground Works

To prevent damage to soil structure, no works concerned with the stripping, moving, spreading or otherwise handling or traversing of topsoil shall be carried out when the site is wet, waterlogged or in periods of drought when dust may be generated. The Contractor shall, if in the opinion of the Contract Administrator weather and ground conditions are unsuitable as above described, and if so instructed by the Contract Administrator, cease all operations. Any delays so caused shall be at no cost to the Employer. If the Contractor should proceed with operations after being so instructed he shall do so at his own risk.

3.	PLANTING: GENERAL CONDITIONS

3.1	Plants are to be provided and planted according to the drawings and schedules provided.

3.2	EAST SUSSEX COUNTY COUNCIL HAS A POLICY TO CONSERVE PEATLANDS. ONLY STOCK THAT IS CONTAINERISED IN PEAT FREE COMPOST WILL BE ACCEPTED.

3.3	Where coir is provided it shall be obtained from a quality controlled source. All composts shall be free of toxic material and components that are harmful to persons or animals. Sewage sludge, household waste and their derivatives shall not be acceptable. The Contractor shall return with his tender the analysis of the compost.

3.4	Substitutes

All plants supplied shall be exactly true to name as shown on drawings. No substitutes from the plant schedules will be allowed except with the written agreement of the Contract Administrator.

3.5	Plants supplied shall have been grown from the Contractor 's own nursery or obtained from a nursery of equivalent standing or obtained from a nominated nursery. The Contractor shall notify the Contract Administrator of his intended source(s) of supply.

3.6	Planting is to be carried out in accordance with the specification and drawings. The right is reserved to adjust the exact position of trees and specimen shrubs after they have been set out on the site. The number of each species and variety to be distributed over the area allocated in a uniform manner, making due allowance for adjacent groups and for the growth habit of each specie or variety.

3.7	The Contractor is to allow for all labour in connection with the supply of trees and shrubs, for planting, including delivery, unloading and placing out.

Plant Handling

3.8	All trees and plants to be carefully packed and if balled up, kept so, to ensure, as far as possible that no damage occurs during loading, transit and unloading, or adverse weather conditions. If, however, roots, shoots or branches suffer slight damage prior to planting, they are to be carefully pruned.

3.9	Any plants or trees that suffer severe damage, through any cause prior to planting, will be rejected and shall be replaced at the Contractor's expense. The Contractor shall ensure that plants retain a moist fibrous root system and that by appropriate treatment plants are protected from the effects of drying out, heat, waterlogging or physical damage during the period between lifting and planting on site. No stock will be accepted by the Contract Administrator on the site unless he is satisfied that plants have been properly protected and that they have been transported to the site in a properly covered vehicle.

3.11	Plants and trees are to be planted at the same depths as those at which they have been previously growing in the nursery. Great care is to be taken to ensure that the root system is not damaged during planting, and the soil is properly firmed around the roots when planting. All planting pits should be finished slightly proud of adjoining surfaces.

3.12	All planting pits are to be well watered prior to planting.

3.13	After planting, ground including shrub and tree pits is to be lightly forked over and/or raked, as the Contract Administrator directs, to bring the surface to a moderately fine, weed-free tilth and approved camber.

3.14	The container-grown shrubs must have been containerised at least during the previous dormant season in containers large enough to hold the root growth and filled with suitable compost. Before planting commences the plants should be thoroughly soaked with water and care is to be taken to avoid root damage when removing the container before planting.

4.	STOCK

4.1	All stock must comply with the current edition of B.S. 3936 and the Contractor shall notify the Contractor Administrator of his intended source(s) of supply.  All root systems must be adequate in relation to the size of the plant and conducive to successful transplantation. The Contractor Administrator reserves the right to view stock prior to delivery to site and reject any poor quality material at any time.

4.2	Specification of Trees

Circumference of stem	Minimum		Approx. upper	Clear stem

measured 1m from		overall height		overall height		height from

ground level			from ground level	from ground level	ground level

Light standard

60mm-80mm			2500mm		2750mm		1500-1800mm

Standard

80-100mm			2750mm		3000mm		1800 minimum

4.3	Balled roots to conform to Appendix A and B of B.S.3936 Part 10.

4.4	Balled roots to conform to Appendix A and B of B.S.3936 Part 10.

4.5	All shrubs, both open ground and containerised shall be supplied according to Section 12 of the above-mentioned British Standard.  Heights and sizes shall be not less than specified in the planting schedule forming part of this specification.

4.6	Bulbs

All bulbs to be of the size specified, dry (unless specified "in the green"), undamaged and disease free.

5.	PLANTING OPERATIONS

5.1	Trees

The Contractor shall excavate tree pits 900mm diameter x 600mm minimum for light standard trees and a pit of adequate size for root spread of all other size trees. The bottom 150mm of each pit shall be well broken up, and any rubble, debris, stones, etc., larger than 75mm found in the excavated material shall be removed from the site.

5.2	Each tree to be planted centrally in its pit after erection of the stake. Roots shall be carefully spread out and well firmed in as material is replaced in the pit.

5.3	Backfill shall consist of excavated material well mixed with an approved PEAT-FREE planting compost to the manufacturer's recommendations.

5.4	Importation of Topsoil for Tree Pits

The Contractor shall allow for importation of approved topsoil for backfill of tree pits.

5.5	Topsoil Specification

Topsoil

All topsoil shall be good quality, clean, loamy medium textured, fertile and with a good humus and fibre content: free of weeds, couch grass, large stones, lumps of clay, rubble, rubbish or other alien material. Imported topsoil should also have the same PH value as existing topsoil on site and meet fully all requirements, and approved by the Contract Administrator prior to being tipped on site. Any topsoil brought on site without a sample having been approved shall be at the Contractor 's own risk. All loads must be of similar quality to the approved sample.

Price per m3  £

5.6	Shrubs, Ground Cover

After setting out plants in an evenly spaced pattern within the planting area, the Contractor shall excavate holes according to the size of the plant. Each plant shall be planted at the same level at which it was previously growing. Except in the case of container-grown stock, roots shall be carefully spread out and packed round with finely broken soil. All plants shall be set upright and shall be well firmed in. Backfill shall consist of excavated soil and an approved PEAT-FREE planting compost to the manufacturer's recommendations, well mixed together. "Enmag" shall be applied in accordance with manufacturers instructions.

5.7	Specimen and Climber Pits

The Contractor shall excavate pits 600 x 600mm diameter and cart subsoil off site. Backfill shall be as for shrubs and ground cover.

5.8	Climber Fixing

The Contractor shall supply -

5.9	Rhododendrons

Each station for a single rhododendron or group of roses shall have 100mm (4") of well rotted farmyard manure well dug into the prepared holes before planting.

5.10	Watering

All trees and shrubs are to be well watered in immediately after planting.

5.11	Bulbs

The Contractor shall supply and plant bulbs in October in areas of shrub beds and beneath areas to be turfed.

5.12	Mulching

The whole area of shrub and individual tree pits shall be mulched with a minimum of 100mm (4") of composted whole tree mulch.  This mulch shall have sufficient structure to withstand windy conditions and shall be moist prior to application.  100mm shall mean a 100mm minimum thickness after natural compaction by subsequent settlement after rain or watering.

At the edge of the planted area, the surface level of the mulch shall be maintained 25-30mm below the adjacent grass or hard surface in order to minimise creep of mulch onto adjacent hard surfaces.

The contractor shall state type and name of mulch product and provide a rate per square metre and a total price for this operation –

The Contractor shall state type and name of mulch product –

£   ............m2.									£

During subsequent weeding care shall be taken not to incorporate the mulch with the topsoil by hoeing but to leave the full thickness on the surface.

5.13	Mulch Mats

All trees and shrubs are to be fitted with mulch mats which the contractor is to supply and fit as detailed below.  Mulch mats to be black woven polypropylene mats – size 1m x 1m well secured to the ground by digging into the soil at all four corners and by pegging with a minimum of 5 metal J-pins per mat 1 peg to be used on the join.  Supplied from English Woodlands, Cross in Hand, Heathfield, East Sussex (Tel. 01435 862992) or other approved.

The contractor shall be entirely responsible for ensuring the mats are well secured (note that the site is very exposed) and must carry out any further measures required to secure the mats at the contractors cost.

5.14	Stakes

All trees and pines are to be secured to a straight pointed stake of 75mm - 100mm average diameter of tanalised larch, or peeled chestnut. Stakes shall have a clear height of 600mm

OR

a suitable height for each tree above the ground and 750mm below ground. The 750mm below ground (if chestnut) being tarred or treated with an approved preservative not less than 3 days before being fixed in the ground. The stake is to be driven into the ground before the tree is planted on the windward side of the tree.

5.15	Mowing Stakes

The Contractor shall supply 2 no. extra mowing stakes -      height   -         diameter placed round each tree to form a triangle. Specification as clause .........

5.16	Tree Ties

The tree is to be tied to the stake with 1    OR   2 No. approved expandable rubber ties with solid rubber spacing hollowed on two sides and twice slotted for tie. The tie is to be strapped around tree and spacer and nailed to the stake with galvanised nails.

1   OR   2 No. ties shall be used for each stake.

Type -

5.17	Temporary Protective Fencing

The Contractor shall supply and erect a chestnut pale fence to the specification shown on Drawing No.

OR

and in the position shown on Drawing Nos.

Price per linear metre £ .............						£

5.18	Windbreak Fencing

The Contractor shall supply -

Price per linear metre £ .............						£

5.19	Rabbit Guards

5.19.1	Spirals

The contractor shall supply and fit recycled plastic transparent 600mm high, 38mm diameter rabbit spirals to each tree except coniferous species from an approved source.

The spiral shall be fitted in accordance with the manufacturers instructions.

The Contractor shall supply and fit a stout bamboo heavyweight cane 900mm in length inserted into each spiral and fitted to the tree to provide support.

The spirals must be well secured.  Any further measures required to secure the spirals shall be carried out at the contractors cost.

All works carried out to the satisfaction of the Contract Administrator.

5.19.2	Netlon Guards

The contractor shall supply and fit circular netlon guards of sufficient diameter to avoid distortion of the plant, to each shrub and coniferous species.  The contractor shall supply and fit a support of 1 no. 900mm, chestnut pale to each guard.

The guards must be well secured.  Any further measures required to secure the spirals shall be carried out at the contractors cost.

All works carried out to the satisfaction of the Contract Administrator.

6.	GRASS SEEDING

6.1	The Contractor shall grass seed during mid-August to October: otherwise in April. Seeding operations shall only take place under suitable weather conditions: as approved by the Contract Administrator.

6.2	Cultivation

The Contractor is to cultivate all areas to be seeded to a minimum depth of 100mm (4"). Stones over 50mm in any linear dimension are to be removed from the surface. The Contractor is to ensure that all pernicious weeds are removed from the site, and that the site is weed-free, firm the seed bed lightly, and reduce to a fine tilth 25mm in depth. All finished levels are to be even running levels, and shall conform to all contours or spot heights shown on the plan.

6.3	Fertiliser

3-5 days before seeding, an approved general pre-germination fertiliser such as fine grade bonemeal/Fisons PS5, or equivalent, is to be supplied, spread and worked into the final tilth, of all proposed grass areas, by the Contractor at the rate of 70g per sq.metre (2 ozs. per sq.yard) or, according to the manufacturers instructions.

6.4	Seed

The Contractor shall supply seed mixture as specified below, which shall be approved by the Contractor Administrator. Seed is to have a germination capacity of not less than 80% and purity of mixture of not less than 90%. The Contractor is to supply the Contractor Administrator with a certificate of purity prior to sowing.

Seed Mixture  -

6.5	Sowing

Seed shall be sown by the Contractor over all grass seeding areas at a rate of    -    g/m2 by means of two equal sowings in transverse directions. After sowing, the ground is to be raked or chain harrowed. The ground is then to be lightly consolidated by rolling with an approved flat roller.

6.6	Failure to Germinate

No payment shall be made to the Contractor should the seed fail to germinate, in whole or in part. The Contractor shall re-seed until a good even sward is obtained to the certified purity and germination capacity, and to the satisfaction of the Contract Administrator.

7.	TURFING

7.1	All turf and turfing operations shall conform to B.S.3969:1965, and B.S.4428:1969, unless otherwise specified. Turfing shall only take place under suitable weather conditions, as approved by the Contractor Administrator. Turfing shall take place preferably during autumn/early winter, not during late spring or early summer unless otherwise approved.

7.2	Cultivation

The Contractor shall cultivate all areas to be turfed to a minimum depth of 75mm (3"), firm lightly and reduce soil to a fine tilth, 25mm in depth. All finished levels are to be even running levels, and shall conform to all contours or spot heights shown on the plan.

7.3	Fertiliser

The Contractor shall apply a general pre-turfing fertiliser, such as fine grade bonemeal/Fisons PS5, at a rate of 70 g/m per m2 (2 oz. per sq.yard) or, to the manufacturer's instructions.

7.4	Supply Turf

The Contractor shall provide and lay good quality meadow or downland turf, fibrous, well rooted, mown and free from matted or dead grass and pernicious weeds following treatment by a selective weedkiller not more than three months previously and cut 405mm x 1350mm - 16" x 54" - (or 900 x 300mm - 3' x 1') of regular size and not less than 25mm (1") in even thickness throughout. The supplier is to keep the grass cut and rolled on the field of origin until deliveries have been completed.

7.5	Turf Samples

Samples of turf are to be submitted to the Contractor Administrator for approval and the origin stated. The samples are to remain intact until turfing is completed. The quality of turf must be maintained throughout with the sample load, and is all to come from the same source:  any deliveries below the standard of the approved load will be rejected and must be lifted (if laid) and carted away from the site at the Contractor's own expense.

7.6	Laying Turf

Turves are to be unloaded on an area clear of that to be turfed unless otherwise sanctioned by the Contractor Administrator. Turves are to be laid in rows on the prepared bed of soil commencing at the near end of the area and laid progressively by placing planks over the last row of turves laid and laying subsequent turves therefrom; the planks to be moved forward as each line of turves is laid and so on to the end of the area. Turves from the pile as unloaded to be wheeled to turf layers on three rows of planks laid closely side by side. The turves to be laid with half lapped joints, well butted up and evenly beaten twice over the whole area, with wooden turf beaters (upright or oblique handled pattern) as approved by the Contractor Administrator. The bottom of the beaters to be frequently scraped clean of accumulated soil or mud. No roller is to be used unless so directed by the Contractor Administrator. Any inequalities in finished levels owing to variation in turf thickness or unequal consolidation of soil to be adjusted after first beating by raking and/or packing fine soil under turves to obtain an even surface to the whole.

The finished levels of turf abutting paving or top of kerbs must not be less than 25mm (1") above surface of paving or top of kerb after laying and beating operations are completed. Turf edges of borders, beds and margins are to be carefully trimmed square and true to line.

No turf is to be lifted or laid in exceptionally dry or frosty weather or in weather conditions otherwise deemed unsuitable by the Contractor Administrator.

7.7	Pegging

The Contractor shall supply -

to banks.

7.8	Watering

The Contractor shall water the turf regularly by means of a sprinkler during dry periods until the turf and the soil beneath is well soaked, to ensure normal growth and establishment. Watering, to the satisfaction of the Contractor Administrator, shall continue until maintenance is completed.

7.9	The Contractor shall be entirely responsible for the successful establishment of turf and will replace any turf lost during the maintenance and establishment period.

8.	MAINTENANCE OF GRASS AREAS

8.1	Seeded Areas

8.1.1	Areas which have been seeded shall receive a light roll once the grass has reached 25mm in height. Any stones, debris etc. larger than 50mm in any dimension which have come to the surface shall be removed at the same visit.

£

8.1.2	The first cut shall take place once the grass has reached 50mm in height. Using a rotary mower, the height of the sward shall be reduced by between one third and one half.

£

8.2	Turfed Areas

8.2.1	Areas which have been turfed shall receive a first cut once the grass has reached 50mm in height using a rotary mower. The height of the sward shall be reduced by between one third and one half.

£

8.3	All New Grassed Areas

8.3.1	Three further cuts shall be carried out at suitable intervals to maintain all grass areas at a height of between 30 - 50mm before those areas are offered for handover.

£

8.3.2	The Contractor shall allow for the adjustment of levels if necessary in order to achieve even running levels throughout the newly grassed area, using a suitable horticultural technique approved by the Contract Administrator.

£

8.3.3	The Contractor  shall allow for the application of an approved selective herbicide to ensure that newly grassed areas are free from pernicious weeds.

£

8.4	Existing Grassed Areas

8.4.1	Grass shall be cut at suitable intervals to maintain all grass areas at a height of between 30-50mm.

£

8.5	All Grassed Areas

8.5.1	The entire area of grass shall be cut without ridges or ribbing, removing all bents and stalks, leaving no areas uncut between rows. An even height of cut shall be produced across the whole area ensuring that all cuttings are evenly distributed. The Contractor  shall cut as closely as possible around obstacles, margins and edges to the same standard and at the same visit.

8.5.2	Equipment used shall be appropriate to the size and gradient of the area, correctly maintained, set and sharpened, and with all guards in place.

8.5.3	Any cuttings which fall onto paths or other hard surfaces shall be swept up and either distributed evenly on the grass surface or removed to the Contractor 's tip. Excessive cuttings shall not be permitted to fall onto shrub/herbaceous areas.

8.5.4	Grass shall not be cut when ground/weather conditions are unsuitable, e.g. through waterlogging/frost or snow.

8.5.5	Should damage be caused to the surface or levels of the grass area due to mowing operations, this shall be repaired to the reasonable satisfaction of the Contract Administrator at the Contractor 's cost.

8.5.6	All litter shall be removed from grass areas prior to the commencement of mowing operations and removed to the Contractor's tip.

8.6	Lawn Edges

8.6.1	At each visit, the edges of grass areas where they abut shrub/herbaceous areas shall be clipped with long handled edging shears. Excessive cuttings shall be spread evenly on grass areas or removed to the Contractor 's tip. UNDER NO CIRCUMSTANCES SHALL A STRIMMER BE USED FOR THIS OPERATION.

£

8.7	Maintenance of grassed areas where this exceeds initial 4 cuts

8.7.1	The Contractor shall maintain the grassed areas at a height of 20-40mm between April-October and at 30-50mm for the remaining year.

The Contractor shall maintain regularly playing field and large amenity areas at 20-40mm.

The Contractor shall maintain rough grass areas at 50-100mm.

The Contractor shall maintain Wild Areas, cutting sward in July and November/December.

Otherwise all operations shall be carried out to conform with paragraphs 9.5 and 9.6 above.

OR	.........................

8.7.2	Fertiliser

The Contractor shall apply an additional approved fertiliser in  ............

8.7.3	Watering

The Contractor shall water grass areas to field capacity if necessary during dry periods. The Contractor  shall allow for adequate watering visits to ensure successful establishment of grass.

£

8.7.4	Approval of the Sward

The sward is to be approved by the Contract Administrator before the Contractor's responsibility is deemed complete.

9.	MAINTENANCE

9.1	East Sussex County Council requires a high standard of after-care and the way in which maintenance operations are carried out shall reflect this. No payment will be made for any maintenance operation that the Contractor fails to complete to the reasonable satisfaction of the Contract Administrator. The Employer reserves the right to employ another Contractor to remedy any deficiencies, the cost of which will be deducted from any retention or other sum due to the Contractor.

In addition to the requirements of clause 2.1 `Notice of Intention', the Contractor shall return a completed copy of the enclosed `Record of Maintenance Visit' to the Contract Administrator by fax or first class post on completion of a maintenance visit.

NO PAYMENTS WILL BE AUTHORISED FOR ANY MAINTENANCE OPERATIONS UNLESS THIS REQUIREMENT IS COMPLIED WITH.

The following operations shall be carried out over the period of ................ calendar month(s) following the certified date of practical completion. A price shall be offered where indicated for each operation.

9.2	Lawn Edges

At each visit, the edges of grass areas where they abut shrub/ herbaceous areas shall be clipped with long handled edging shears. Excessive cuttings shall be spread evenly on grass areas or removed to the Contractor 's tip. Under no circumstances shall a strimmer be used for this operation.

9.3	Wild Flower Areas

9.3.1	Following a successful autumn sowing, in the first year only, wild flower areas shall be cut on 3 occasions. In early April, the area shall be mown at height of 50-75mm with a rotary mower, removing the cuttings to the Contractor 's tip. During the second half of July, and again during November, this operation shall be repeated, however the cuttings shall be left for a fortnight, then collected and removed to the Contractor 's tip.

£

9.3.2	Pernicious weeds shall be spot treated with a glyphosate based C.D.A. herbicide during April and June.

£

9.4	Trees/Shrubs/Herbaceous/Hedges

The following maintenance operations shall be carried out with the joint aims of encouraging rapid establishment of new plantings and maximising their decorative and functional effects.

9.4.1	Monthly, during the months of March, April, May, June, July, August, September, October and November, the following works shall be carried out.

9.4.1.1	Annual and ephemeral weeds shall be removed by hand and perennial weeds spot treated with a glyphosate based C.D.A. herbicide or weedwiper system. Care must be taken to avoid damage to the new planting and to avoid mixing mulching material with the topsoil.

£

9.4.1.2	Litter, rubbish and all arisings shall be removed to the Contractor 's tip.

£

9.4.1.3	Plants loosened by the effects of wind, frost heave, etc., shall be set upright and re-firmed.

9.4.1.4	Pruning of shrubs and climbers shall be carried out by competent staff, using appropriate equipment correctly set and sharpened, in accordance with the needs of each variety and individual plant. Generally in the first year after planting, pruning should be restricted to the removal of any dead, diseased, weak or straggly growth, and to prevent any encroachment over paths, roads and other hard surfaces, lawns, and windows, where this is likely to impede clear passage or obstruct light. Where the intention of the landscape designer is to soften hard edges where planting meets other surfaces pruning shall be carried out sensitively to achieve this aim.

Unless otherwise instructed each plant shall be allowed to develop its natural habit and shape and pruning shall be carried out with this in mind. UNDER NO CIRCUMSTANCES SHALL A HEDGE TRIMMER BE USED FOR PRUNING.

£

9.4.2	Following die-back in the autumn, dead vegetative material shall be removed carefully from herbaceous plants in November. Subjects featuring decorative seed heads shall be dead headed and cleaned up in March, prior to the commencement of new growth. All arisings shall be removed to the Contractor's tip.

£

9.4.3	Within the fortnight preceding final handover, an application of Enmag shall be made to the entire area of tree/shrub/herbaceous/hedge planting during March at a rate of 70g/m2 and lightly worked into the surface of the mulch.

£

9.4.4	Again, within the fortnight preceding final handover, the mulch layer shall be topped up to the specified depth using the originally specified material.

£

9.4.5	At the edge of the planted area, the surface level of the mulch shall be maintained 25-50mm below the adjacent grass or hard surface. This operation shall be carried out in addition to normal edging operations. Any mulch which has crept onto surrounding grass or hard areas shall be swept back onto planted areas.

£

9.4.6	Between the time of planting and final handover, any plant material which dies, or is not in a thriving condition, whether due to the effects of weather, lack of water, poor pruning technique, lack of maintenance, herbicide damage, or any other cause except that due to vandalism beyond the control of the Contractor shall be replaced by the Contractor  at his own cost.

Planting conditions being favourable, and the time of year being appropriate, replacement planting shall be continual throughout the contract period so that at handover, the originally specified quantities and varieties are present.	£

9.4.7	Vandalised plant material shall be replaced by the Contractor at the scheduled rates at the cost of the Employer on the written instructions only of the Contract Administrator.

9.4.8	The Contractor shall water all planted areas and individual trees and shrubs in grass to field capacity of the full cultivated depth as required to ensure the healthy establishment of all stock at all times during the maintenance period.	£

9.4.9	New Hedges

The designed height and width of the new hedge is ..............m high and .............m wide. Any necessary formative pruning in the first year shall be carried out using secateurs with these dimensions in mind.	   £

9.4.10	Existing Hedges

Vertical faces shall be trimmed perpendicular and true to line so as not to overhang paths, roads, and other hard areas, lawns or planting areas. Tops shall be cut horizontal to the point of the last cut, unless otherwise instructed. A flail cutting shall not be used without the approval of the Contract Administrator. Large leafed species, for example Prunus laurocerasus or Aucuba ssp. shall be trimmed using secateurs unless otherwise instructed. Self-sown trees and shrubs, brambles and other weed growth, litter and rubbish shall be removed. All arisings shall be taken to the Contractor 's tip. Hedges shall be cut twice per year, once in June and once in October.

£

9.4.11	Trees

All stakes, ties, guards, mulch mats, etc., shall be checked each time the Contractor visits the site and adjusted, repaired or renewed as necessary, at the Contractor 's expense.

£

9.4.11.1	All epicormic growth, suckers, dead and diseased or damaged branches shall be cut back to a good bud or branch during November.

£

9.4.12	Wall Wiring

9.4.12.1	Wall wiring shall be maintained in sound condition throughout the maintenance period. Broken wires, or galvanised vine eyes which develop rust, shall be replaced at the Contractor 's expense.

Climbers shall be tied in regularly throughout the period.	£

25 November 2013

Ref:  LA08-1

SCHEDULE OF SUPPLY AND PLANT/WORKS FOR

| No. | Description | Size (in mm) | UNIT £ p | TOTAL £ p |
| --- | --- | --- | --- | --- |

SUMMARY

Preliminaries including P.C.,

Provisional Sums and

Contingencies	£

Schedule of Works	£

TOTAL (excluding Value Added Tax) carried to	   ______

Form of Tender 	£ ______

Amount of Value Added Tax payable   £

This sum is NOT to be included in the Tender Total.

SIGNATURE

TRADE NAME

ADDRESS

DATE